## Slide 1
BSides Vancouver · Workshop
The Last-Minute Badge
That Actually Worked
▌ Software Edition
Nick Maltchev · Mirai Security
Sandy — original design and firmware PoC. Kirk — hardware engineering. Nick — firmware 2.0.
Sun May 31, 2026
9:30 — 11:30 PDT
Room 1700

## Slide 2
What you're here for
✓
A working badge
Yours to keep.
⤓
Source + schematic + binaries
Everything on GitHub. MIT licensed.
⛭
A mental model
What the firmware does, where to change it, and where the landmines are.
✎
A sandbox to break
A starter template that builds out of the box, plus the full firmware to extend.
❯ github.com/maltchev/bsides-vancouver-badge
The Last-Minute Badge That Actually Worked
2 / 24

## Slide 3
The hardware in one slide
ESP32-C3
RISC-V · 160 MHz
4 MB flash · WiFi / BLE
on-chip USB Serial / JTAG
ST25R3911B
NFC reader · 13.56 MHz · SPI
5 × WS2812B
addressable RGB chain · 1 GPIO
Charlieplex
6 LEDs through 3 GPIOs
Hall MGH201
bipolar latch · active-LOW
ALS-PT19
ambient light · analog
BTN1 / BTN2
BTN2 wakes from sleep
Power: USB Type-A · 2 × CR2032 in parallel
The Last-Minute Badge That Actually Worked
3 / 24

## Slide 4
Why these choices
COMPONENT
WHY THIS PART
ESP32-C3
RISC-V, on-chip USB Serial / JTAG, WiFi + BLE, ~$1.50 in quantity.
ST25R3911B
Full NFC reader IC. Reads cheap printable NFC-V cards.
WS2812B
One GPIO drives the whole RGB chain. ~60 mA per LED at full white.
Charlieplex LEDs
3 GPIOs drive 6 LEDs. Saves pins and BOM cost.
MGH201A1T3
Bipolar Hall latch. (Behaviour covered later — it surprised us.)
2 × CR2032
Wearable power. (Coin-cell brownout covered later.)
The Last-Minute Badge That Actually Worked
4 / 24

## Slide 5
The stack
YOUR CODE
main.cpp · badge_state · wifi_portal
ARDUINO
digitalRead, delay, FastLED, RMT5 driver
ST NFC stack
RFAL + ST25R3911B driver
ESP-IDF v5.4.1
FreeRTOS · lwIP · esp_wifi · http_server · NVS · sleep
The Last-Minute Badge That Actually Worked
5 / 24

## Slide 6
Repository layout
bsides-vancouver-badge/
├── README.md LICENSE CHANGELOG.md ← project metadata
├── version.txt ← human-readable firmware version
├── CMakeLists.txt sdkconfig.defaults ← ESP-IDF project root
│
├── main/ ← the workshop firmware
│ ├── main.cpp ← entry, main loop, NFC + sensors + LEDs
│ ├── project_pins.h ← pin map + tunable constants
│ ├── badge_state.h/.cpp ← NVS persistence
│ └── wifi_portal.h/.cpp ← optional WiFi AP + control panel + CTF
│
├── components/ ← vendored: Arduino, FastLED, NFC
│
├── starter-template/ ← blank canvas — your sandbox
├── prebuilt/2025-production/ ← last year's firmware as .bin
└── docs/ ← BUILDING / HARDWARE / SOFTWARE / NFC_TAGS
The Last-Minute Badge That Actually Worked
6 / 24

## Slide 7
Boot flow
1
initArduino()
bring up Arduino layer (delay, digitalRead…)
2
log reset reason
POWERON · BROWNOUT · PANIC — useful when things go wrong
3
BTN2 held? wipeAll()
hard-reset escape hatch — flash red while held
4
pinMode + FastLED
every peripheral configured · rainbow boot show
5
BadgeState::restoreAll()
NVS → live state (colors, attendance, brightness)
6
checkAndApplyMasterUnlock()
if all challenges done, light RGB[3] BSides-orange
7
rfal_nfc.rfalNfcInitialize()
bring up NFC reader — TX power written separately
8
for (;;) loop();
into the main loop, forever
The Last-Minute Badge That Actually Worked
7 / 24

## Slide 8
The main loop
void loop() {
refreshAwakeIndicator(); // RGB[0] green or blue
drainCtfFlag(); // celebrate if CTF was solved
checkHallEffectSensor(); // magnet present? update HALL_LED
checkLuxSensor(); // bright / dark / hold puzzle
CLEDDisplay(); // refresh one charlieplex slot
checkButtons(); // BTN1 scan, BTN2 activity / WiFi
handleSleepGating(); // inactivity / pocket sleep
rfal_nfc.rfalNfcWorker(); // NFC stack background
runNfcStateMachine(); // discovery → tag → done
}
Single thread.
No FreeRTOS tasks of our own. Eight calls, in order, every iteration. Trade-off: a slow function stalls the rest.
The Last-Minute Badge That Actually Worked
8 / 24

## Slide 9
State persistence
NVS namespace 'badge'
namespace BadgeState {
void restoreAll();
void saveTeamColours(); // RGB[1], RGB[4]
void savePresentationProgress(); // counter + bits
void saveMalwareFlag(); // V-tag attendance
void saveBrightness(); // 0..255
void saveRgb1() / saveRgb3() / saveRgb4();
bool firstBootCheckComplete();
void markFirstBootCheckComplete();
void wipeAll();
}
Design rules
Every save is write-through. Keys match the v1 firmware byte-for-byte — a v1 badge keeps its state when re-flashed with v2.
The Last-Minute Badge That Actually Worked
9 / 24

## Slide 10
Configuration knobs · project_pins.h
#define INACTIVITY_TIMEOUT_S 60 // idle seconds before light sleep
#define HALL_HOLD_DURATION_MS 2500 // hold magnet this long → puzzle fires
#define HALL_DEBOUNCE_MS 200 // filter stray magnetic fields
#define LUX_DARK_THRESHOLD 120 // analog < this = covered
#define LUX_POCKET_SLEEP_MS 60000 // dark this long → in-pocket sleep
#define BADGE_DEBUG_NO_SLEEP 0 // 1 = disable sleep (USB monitor)
#define BADGE_LOW_POWER 0 // 1 = skip NFC + drop to 80 MHz
DEBUG_NO_SLEEP = 1 · serial-monitor mode
LOW_POWER = 1 · coin-cell mode
The Last-Minute Badge That Actually Worked
10 / 24

## Slide 11
WAR STORY #1
The NDEF crash
First card scanned after the v2 refactor → fault
✖ Guru Meditation Error
MTVAL=0x000005fc
ndefT5TPollerAccessMode line 149
Backtrace:
ndefPollerReadRawMessage()
ndefT5TReadCC()
ndefT5TPollerAccessMode()
What was happening
The constructor wrote a this pointer to ONE offset inside ndefContext. The library tried to read it back from a DIFFERENT offset. Two translation units disagreed on the layout of the same struct. Classic C++ ODR violation.
The Last-Minute Badge That Actually Worked
11 / 24

## Slide 12
WAR STORY #1
The fix: one line of CMake
Force both translation units to compile with the same feature flags
main/ — our custom flags
#define RFAL_FEATURE_LISTEN_MODE false
#define RFAL_FEATURE_WAKEUP_MODE true
#define RFAL_FEATURE_ISO_DEP_LISTEN false
#define RFAL_FEATURE_ISO_DEP_APDU_MAX 1024
components/NFC_RFAL/ — library default
#define RFAL_FEATURE_LISTEN_MODE true
#define RFAL_FEATURE_WAKEUP_MODE false
#define RFAL_FEATURE_ISO_DEP_LISTEN true
#define RFAL_FEATURE_ISO_DEP_APDU_MAX 512
Add main/ to the library's private include path:
# components/NFC_RFAL/CMakeLists.txt
set(priv_includedirs ${CMAKE_CURRENT_LIST_DIR}/../../main)
The Last-Minute Badge That Actually Worked
12 / 24

## Slide 13
WAR STORY #2
The Hall sensor that wouldn't let go
We assumed a unipolar switch. We got a bipolar latch.
WHAT YOU DO
WHAT THE PIN DOES
S-pole magnet near sensor
line pulled LOW
Magnet removed
stays LOW (latched)
N-pole magnet near sensor
line released HIGH
Magnet removed
stays HIGH (latched)
MGH201A1T3 is a bipolar LATCH, not a switch.
The Last-Minute Badge That Actually Worked
13 / 24

## Slide 14
WAR STORY #2
The fix: remove SOS Morse
HALL_LED now follows the sensor's latched state directly
One polarity → LED on
Reverse polarity → LED off
Remove magnet → state held
- checkSosMorse();
+ CLED_State[HALL_LED] = hallDebounced ? ON : OFF;
The Last-Minute Badge That Actually Worked
14 / 24

## Slide 15
WAR STORY #3
Console dies on light sleep
USB Serial / JTAG on the ESP32-C3 is an on-chip peripheral, not an FTDI
AWAKE
host sees device, COM7 open in PuTTY
LIGHT SLEEP
USB peripheral powers DOWN → host sees DISCONNECT
WAKE
device re-enumerates → maybe new COM port, PuTTY session dead
Workarounds
① Unplug + replug USB to force a clean enumeration before flashing. ② Hold BTN1 (= GPIO 9 boot strap) while plugging in to force ROM bootloader. ③ Set BADGE_DEBUG_NO_SLEEP = 1 while you're actively monitoring.
The Last-Minute Badge That Actually Worked
15 / 24

## Slide 16
WAR STORY #4
NFC silently dies after the first sleep cycle
The ST25R3911B's protocol state drifts during the SPI silence of light sleep
Symptom
1. Boot. Scan tag. Works. 2. Idle 60 s → light sleep. 3. Press BTN2 → wake. 4. Scan tag → no response. No error logged. Just silence.
Fix — re-init NFC after every wake:
// inside our wake-up handler:
ReturnCode err = rfal_nfc.rfalNfcInitialize();
if (err == ERR_NONE) {
rfst25r3911b.st25r3911WriteRegister(
0x2A, 0xF8); // restore TX power
state = BADGE_WAIT_FOR_BUTTON;
ESP_LOGI(TAG, "NFC re-init OK");
} else {
ESP_LOGW(TAG, "NFC re-init FAILED");
}
The Last-Minute Badge That Actually Worked
16 / 24

## Slide 17
WAR STORY #5
Brownout on coin cells
Supply can't deliver the NFC inrush. Chip resets in a loop.
Light show
→
BadgeState restore
→
NFC init → current spike
→
VDD sags < 2.51 V
→
Brownout reset
↻ repeat forever
The numbers
• 2 × CR2032 in parallel ≈ 20 Ω internal resistance. • ESP32-C3 brownout-detect threshold ≈ 2.51 V. • ST25R3911B oscillator + analog FE inrush > what the cells can deliver. • Supply sags below 2.5 V → BOD trips → chip resets → repeat.
The Last-Minute Badge That Actually Worked
17 / 24

## Slide 18
WAR STORY #5
The compromise: a compile flag
On USB: full firmware. On coin cells: skip the expensive boot path.
// project_pins.h
#define BADGE_LOW_POWER 0 // 1 = battery-friendly mode
// main.cpp
#if !BADGE_LOW_POWER
err = rfal_nfc.rfalNfcInitialize();
rfst25r3911b.st25r3911WriteRegister(0x2A, 0xF8);
#else
ESP_LOGW(TAG, "BADGE_LOW_POWER=1 — NFC SKIPPED (battery mode)");
#endif
On USB
• CPU at 160 MHz • NFC initialized at max TX power • Default brightness
On coin cells
• CPU at 80 MHz • NFC initialization skipped • Lower boot brightness
The Last-Minute Badge That Actually Worked
18 / 24

## Slide 19
WiFi portal
Long-press BTN2 → badge becomes an open AP. Phone gets a captive portal.
SSID: BSidesBadge-XXXX (open, last 4 hex of MAC) · http://192.168.4.1/
GET
/
live control panel (sensors, LEDs, brightness)
GET
/api/state
JSON snapshot — polled by the panel @ 2 Hz
POST
/api/color
set RGB[slot] from the phone, live
POST
/api/brightness
set FastLED brightness 0..255
GET
/ctf
challenge landing page
GET
/ctf/login + POST
intentionally-vulnerable login form
GET
/ctf/dashboard
role-gated by a cookie value
The Last-Minute Badge That Actually Worked
19 / 24

## Slide 20
The CTF — a cookie-tampering challenge
Edit the auth cookie to escalate from guest to admin. Solving it flashes your badge.
What the browser sends
GET /ctf/dashboard HTTP/1.1
Host: 192.168.4.1
Cookie: auth=guest ← edit me
// then change to auth=admin
// in DevTools and refresh
What the server does
// no signing, no encryption,
// no server-side session.
bool is_admin =
strstr(cookie, "auth=admin") != nullptr;
if (is_admin) {
s_flag_captured.store(true);
}
FLAG
BSIDES{cookies_are_not_credentials}
The Last-Minute Badge That Actually Worked
20 / 24

## Slide 21
What you get when you clone
Three buildable entry points
firmware (main/)
The full workshop firmware. What's on your badge right now. Build with idf.py build from the root.
starter-template/
Blank canvas. Hardware boots, light show plays, the main loop is empty. Your sandbox.
prebuilt/2025-production/
Original 2025 firmware as .bin files. Restore the badge without needing ESP-IDF installed.
The Last-Minute Badge That Actually Worked
21 / 24

## Slide 22
Build & flash
Five commands. First build is slow. Subsequent builds are seconds.
git clone https://github.com/maltchev/bsides-vancouver-badge.git
cd bsides-vancouver-badge
idf.py set-target esp32c3
idf.py build
idf.py -p <PORT> flash monitor # COM7 on Windows, /dev/ttyACM0 on Linux
If flash fails with "Failed to connect: No serial data received"
① Unplug + replug USB and try again. ② Or hold BTN1 while plugging USB in (GPIO 9 is the boot strap → forces ROM bootloader).
The Last-Minute Badge That Actually Worked
22 / 24

## Slide 23
Idea menu
docs/WORKSHOP.md has the full list and pointers to answer keys
★
Cycle RGB[0] colour on each BTN1 press.
★
Light an indicator LED while a magnet is held.
★★
Map ambient light → LED brightness in real time.
★★
Write a new NFC tag with TagWriter, scan it, see it dispatch.
★★★
Add a new NFC command (case 'H': ...) to ndefReadTag().
★★★
Add a /api/celebrate endpoint to wifi_portal.cpp.
★★★★
Replace the captive-portal CTF with your own challenge.
The Last-Minute Badge That Actually Worked
23 / 24

## Slide 24
Thanks
Open source, MIT licensed. Pull requests welcome.
❯ github.com/maltchev/bsides-vancouver-badge
ORIGINAL DESIGN AND FIRMWARE POC
Sandy
HARDWARE ENGINEERING
Kirk Richardson
FIRMWARE 2.0
Nick Maltchev